ECE 0142 Computer Organization

Homework 2

Assigned: 1/19/2016  Due: 1/22/2016 before recitation

Name___________________________________________________________________

ID_____________________________________________________________________

- (15 pts) Fill in the table. Write down all possible binary representations for the decimal values in the first column. Assume that you have 5 bits in total. If the number cannot be represented within 5 bits, write “not representable”.

| decimal | 5-bit binary |
| --- | --- |
|  | sign-magnitude | 1’s complement | 2’s complement |
| 0 |  |  |  |
| -1 |  |  |  |
| -16 |  |  |  |
| 16 |  |  |  |
| -2.25 (use 2 digits for fractional part) |  |  |  |

- (6 pts) Show the steps in converting the following floating numbers into single-precision binaries according to the IEEE 754 standard.

-31.187510

s =

e =

f =

The single precision form is:

- (6 pts) Show the steps in converting the following single-precision binaries according to the IEEE 754 standard into decimal FP number.

1 1000 0111 1010…02

s =

e =

f =

The decimal FP number is:

- (6 pts) Show the negative value range of the IEEE 754 floating numbers, considering both normalized and un-normalized representations. Hint, this can be derived from the positive value range.

- (10pts) IEEE 754 can represent same number of FPs between 2n and 2n+1 as 2n+1 and 2n+2. How many FP numbers can be represented in each such interval? Find out the difference between neighboring numbers for interval  (2n , 2n+1). Can you infer from the results if IEEE 754 is better for small numbers or large numbers?